## Slide 1
Automated Thin Section Analysis
Imperial College London Department of Earth Science and Engineering
10th September 2019
ACSE MSc Independent Research Project
Richard Boyne (CID 01057503)

## Slide 2
Automated Thin Section Analysis
Thin Section Images
Project Aims
TSA Software
  Overview
  Algorithms
  Implementation
Results
Conclusions
Questions
Agenda

## Slide 3
Thin Section Images
  Core slices under microscope
  Cross polariser angles give additional insight
  Analysis determines properties (e.g. porosity, grain size distribution)
  High regional variability
Texas Sandstone (300x magnification)
Parallel Polarisers
Cross Polarisers
  Cheap to produce, expensive to analyse
  Various analysis methods:
    Point counting
    Image filters & thresholds
    Watershed transformation
    Machine learning techniques (in development)

## Slide 4
Project Aims
  Develop a python toolset for fast Thin Section Analysis (TSA)
  Software should be:
    Adaptable to develop a range of pipelines
    Sustainable for future development within Wintershall DEA
    Usable with little programming training
    Valid for thin section images
  Optimisation of features and hyperparameters not considered
  TS images cropped for easier development

## Slide 5
Additional: Need for Locality
Example of no locality enforcement on Texas sandstone sample
Contour like behavior seen across the entire image

## Slide 6
K-means
SLIC

## Slide 7
Additional: Color-Position Scaling

## Slide 8
Performance
  (number pixels) largest computation in TSA
  Optimised with vector operations (Pytorch)
  Binning reduces segment dependency
  Changeable distance metric:
Image Size
Number of Segments

## Slide 9
MSLIC
  Combine multiple images in single segmentation
    Changeable combination metric
    Better segmentation in theory
    Image misalignment means worse in practice
MSLIC creating common mask between images
Crossed Image
Parallel Image
Overlap
  Allows for feature extraction from all images

## Slide 10
  Feature extraction defined by user:
  Allows for variable feature selection
  Allows for external clustering algorithms
Segment Clustering
  Unsupervised clustering of segments with common material
  Used to merge over-segmented regions
  Versatile to varying images

## Slide 11
Additional: AGNES Distances
Merging criteria example for AGNES clustering using dummy data 7 clusters (seen before)
7 Clusters

## Slide 12
AGNES
  One of many possible algorithms
  Agglomerative clustering (bottom up)
Example AGNES clustering on 2D dummy data
  Determines number of clusters
  Multiple termination criteria and distance metrics implemented

## Slide 13
Clustering Difficulties
  Distance clustering feature scaling required
  Difficulties combining texture and colour
  Either individually insufficient
  Colour clustering only valid for coarse labelling
  (i.e. rock, pore, clay)
Original Image
Example Cluster 1
Example Cluster 2
  Grain segments clustered separately due to:
    Texture variations
    Natural colour variation
    Differences between images

## Slide 14
Edge Confidence
  Attempt to identify which edges are due to over-segmenting
  Independent from clustering
  Theoretically better for isolating grains
  User defined edge confidence:

## Slide 15
Edge Confidence
Edge Confidence
Scharr edge filter alignment edge confidence
Segmentation from edge based merging

## Slide 16
Additional: All Clusters
All clusters from Thailand image, user input labels them into the clay, rock, pore segmentation shown previously

## Slide 17
Results
Clay Regions
Rock Regions
Pore Regions
Mis-identified pore
Pore too small to be segmented
Reasonable segmentations
However porosity results prove further work needed
Thailand sandstone

## Slide 18
Additional: Porosity Results
  Six regions sampled three times
  Only sandstone considered (subset of expected images)
  Possible issues: under sampling of whole image, mentioned clustering issues, need for correction factors, clustering method insufficient to capture material trends

## Slide 19
Sustainability
  Reusable modular structure
  Good documentation (numpy convention & sphinx)
  Unit & Acceptance testing (Pytest)
  Package formalisation (pip)
  Linted Code (Pylint)
  Frequently commented code
  Hosted on GitHub Pages
  https://msc-acse.github.io/acse-9-independent-research-project-Boyne272/index.html

## Slide 20
Conclusions
  TSA Developed
  Sustainable for future development
  Adaptable
    SLIC distance metric
    MSLIC combination metric
    Clustering features and algorithm
    Edge detection metrics
  Usable for TS analysis pipeline development
  Valid with initial segmentations looking reasonable
  Further Work Needed
  Clustering difficulties
  Edge detection difficulties
  Initial porosity results poor
  Unsupervised clustering may be unable to achieve desired TS automation
  Potential for user based corrections and label storing
  Unconsidered features (e.g. image size)

## Slide 21: Thank you
Questions

## Slide 22
Intro
Project Aims
Over Segmentation
Clustering
Edge Detection
Results
SLIC Locality
SLIC Dist. Metric
AGNES Distances
Pre-label Clusters
Porosity Results